## Slide 1: Advanced Doppler Techniques

## Slide 2: Goals
Flow estimation without direction limitation.
Better differentiation between flow signals and non-flow signals.
Efficient imaging with a wide dynamic range.

## Slide 3: Non-Parallel Flows
Speckle tracking.
Estimation and correction of flow angle by using the Doppler bandwidth resulting from a finite resolution volume.
Estimation of flows perpendicular to the image plane using signal de-correlation.
Three-dimensional flow imaging using multiple probes.

## Slide 4: Speckle Tracking
Performance is limited to signal-to-noise ratio.
Computationally demanding.
Sampling interval needs to be small enough to avoid speckle de-correlation.

## Slide 5: Beam Geometry and Doppler Bandwidth
Assuming a constant velocity flow through the resolution volume, the Doppler bandwidth is proportional to tan
flow direction


## Slide 6: Imaging of Flows Moving Through the Imaging Plane
Commonly seen in intravascular ultrasound.
Conventional Doppler cannot image blood flows perpendicular to the image plane.
flow direction
image plane

## Slide 7: Imaging of Flows Moving Through the Imaging Plane
Flow velocity can be estimated by assuming
  finite slice thickness.
  adequate frame rate.
Velocity is proportional to rate of signal de-correlation.
Cannot estimate the flow direction and the sensitivity is range dependent.

## Slide 8: Imaging of Flows Moving Through the Imaging Plane
Signal de-correlation is estimated by FIR.
Flow information is encoded as in Color Doppler.
depth
firing

## Slide 9: 3D Flow Estimation Using a Triple Beam Lens
3D flow information can be obtained by accurately tracking the blood signals between beams.
Exact beam geometry must be known and the success strongly depends on the lens construction.
Tradeoff between accuracy and velocity range.

## Slide 10: 3D Flow Estimation Using a Triple Beam Lens
Same concept can be implemented by using 2D arrays.
With a 2D array, beam characteristics can be electronically constructed.
With 1D arrays, two-dimensional flows can be similarly estimated.

## Slide 11: Tissue and Blood Differentiation
Signals from blood with low velocities may be interfered by signals from slow moving tissue (e.g., due to respiration).
A wall filter with a sharp transition band is required. However, such a filter often requires more samples, thus decreasing frame rate.

## Slide 12: Tissue and Blood Differentiation
The cut-off frequency of the wall filter varies from one flow state to another. Therefore, it is desirable to be able to track the flow characteristics automatically.
input signal
frequency estimator
wall filter

## Slide 13: Tissue and Blood Differentiation
Signals from tissue in motion appear as “flash” superimposed on top of the B-mode image.
To further differentiate tissue from blood, the signal levels may be used as a differentiator.

## Slide 14: Post-Processing
A threshold is often set for noise rejection. In other words, signals below a particular level are considered noise and the estimated values are not displayed.
A low threshold results in random noise in the image.
A high threshold results in drop-outs.

## Slide 15: Post-Processing
Simple median filters may be used to remove random noise and drop-outs.
Sophisticated spatial or temporal filters may also be required.
Simple linear filters often have effects to the whole image.

## Slide 16: Post-Processing
For Power Doppler, system gains need to be applied (similar to B-mode) properly. Un-proper gain settings are apparent.
For Color Doppler with mapping of two variables, details of the mapping function strongly affect flow presentation.

## Slide 17: IIR Wall Filters
FIR filters are easy to design and guaranteed to be stable.
Compared to IIR filters, FIR filters exhibit a wide transition band. Therefore, more samples are needed for the same accuracy.
IIR filters are of interest to provide narrow transition band with short duration.

## Slide 18: IIR Wall Filters
Typical IIR filters have a long transient response. Therefore, the first few samples of the filter output need to be discarded and the frame rate advantage becomes less significant.
IIR filters may be properly initialized to reduce the transient response.

## Slide 19: IIR Wall Filters
Commonly used initialization techniques:
  zero.
  step.
  exponential.
Note that the particular initialization technique has to be robust under most situations in order to be clinically useful.

## Slide 20: Advanced Spectral Estimation Techniques
FFT is one of the most popular spectral estimation techniques for Doppler Ultrasound.
Parametric, or model based methods have been investigated. The performance has not been consistent due to the non-stationary properties of the signals and the accuracy of the models.

## Slide 21: Advanced Spectral Estimation Techniques
FFT based methods, with adjustable window length and window function, are still the most acceptable. This is partly due to flow presentation.
A combination of several different methods may have potential to improve the spectrum more consistently.