## Slide 1: Increasing Depth of Field

## Slide 2: Depth of Field
Depth of field is defined as the region around the focal point in which good diffraction pattern is maintained.
For pulse echo imaging, since a fixed transmit focus is used per firing, depth of field is closely related to the overall image quality.

## Slide 3: Depth of Field
depth of field

## Slide 4: Depth of Field
Depth of field is defined as the incremental range relative to the focal point for which the phase errors at the ends of the active aperture are within /8
Equivalently, depth of field = 2*f#2*where f# is defined as the ratio of the focal range to the active aperture size,  represents the wavelength.

## Slide 5: Depth of Field
Larger f-numbers or non-uniform apodization are commonly used to increase depth of field (i.e., to improve image uniformity).
Depth of field is gained at the price of loss in lateral resolution.

## Slide 6: Depth of Field

## Slide 7: Multiple Transmit Foci
Multiple transmit foci may be used to increase the depth of field.
It is usually done serially. Therefore, frame rate is reduced.

## Slide 8: Multiple Transmit Focusing
The simplest way of producing multiple transmit foci simultaneously is to combine multiple pulses into a new pulse. The timing is determined by geometry.
This method suffers from interference between different foci.

## Slide 9: Multiple Transmit Focusing
More complicated coded excitations may be used, but success has been limited.

## Slide 10: Non-diffracting Beams
According to Huygens-Fresnel principle, commonly used solutions to the homogeneous wave equation produce diffraction effects.

## Slide 11: Non-diffracting Beams
Alternative solutions can be used such that wave field is not a function of range, i.e., it is diffraction free.
Commonly used solutions include J0 Bessel beam (first kind, zero-th order) and X beam.
There exists a tradeoff between depth of field, aperture size and mainlobe width. Sidelobes are relatively high.

## Slide 12: Retrospective Transmit Focusing
The two-way beam pattern is the Fourier transform of the two-way aperture function.
**
=
F.T.

## Slide 13: Retrospective Transmit Focusing
The effective transmit aperture is the product of the transmit apodization and the defocusing phase term.
To remove the phase errors on transmit, we can apply a pre-detection filter after the beam formation.

## Slide 14: Retrospective Transmit Focusing
In practice, this can be implemented as a set of range dependent pre-detection filters.
probe
buffer
buffer
filter bank
range

## Slide 15: Increasing Penetration

## Slide 16: Coded Excitation
Based on FDA guidelines, both pulse average (SPPA) and temporal average (SPTA) are regulated.
SPPA limit is 190W/cm2, SPTA limit is 720mW/cm2.
Under typical conditions, only one of the limits is reached.

## Slide 17: Coded Excitation
The goal of coded excitation is to increase transmit power without exceeding the regulations and without degrading range resolution.
To create long pulses without degrading range resolution, bandwidth of the transmitted pulse must be maintained.

## Slide 18: Coded Excitation
c0 is a constant, f0 is the center frequency, f is the bandwidth and is chosen such that times the pulse duration is equal to f .

## Slide 19: Coded Excitation
Axial resolution can be improved by compressing the received pulse. This is done either by correlating received signals with a reference signal or by convolving with a filter.
The filter can be inverse or matched.

## Slide 20: Coded Excitation
probe
buffer
buffer
compression filter
range
In general, range lobe levels are determined by filter length

## Slide 21: Coded Excitation
Another application of coded excitation is to reduce peak intensity while maintaining the transmit power.
This is useful for second harmonic applications in which acoustic intensity needs to be lowered in order not to destroy bubbles.