## Slide 1: Non-linear Imaging

## Slide 2: Non-linear Imaging
In most situations, acoustic propagation phenomena are considered linear.
Non-linear phenomena in human tissue are complicated analytically.
Nevertheless, non-linear imaging has emerged as a major diagnostic tool.

## Slide 3: Non-linear Imaging: Clinical Applications
Tissue characterization: tissue of different types exhibits different non-linear response.
Contrast imaging: contrast agents are artificially introduced to enhance visualization of low level signals.
Tissue harmonic imaging: reduce imaging artifacts.

## Slide 4: Tissue Non-linear Response
The interaction between microstructures acts as “non-linear springs” and therefore results in non-linear response.
direction of sound pressure

## Slide 5: Tissue Non-linear Response
Non-linear response depends on tissue structure and the amplitude of the acoustic wave.
The second harmonic signal is of particular importance due to its strength and frequency.

## Slide 6: Non-linear Parameter B/A
The larger the B/A, the higher the non-linear response.

## Slide 7: B/A Parameters: Measurements
Finite amplitude method:
  B/A is related to the second harmonic generation. Thus, it can be found by relating the signal amplitude at the fundamental frequency to the second harmonic component.
Thermodynamic method:
  The B/A value is determined by measuring the change of sound speed with pressure and temperature.

## Slide 8: B/A Parameters: Typical Values
Typical values:
  Water:5.5+/-0.3.
  Liver: 7.23.
  Fat: 10.9.
  Muscle: 7.5.
Results from both methods have excellent agreement.

## Slide 9: Non-linear Propagation
The frequency domain solution to Burgers’ equation:
where 1+B/(2A).

## Slide 10: Non-linear Propagation
Wave at distance z
Linear propagation to z+z
Nonlinear propagation at z+z
angular spectrum method
frequency domain solution to Burgers’ equation

## Slide 11: Second Harmonic Generation by Contrast Agents
Harmonic response is generated by contrast agents, instead of tissue propagation.
It can be modeled as:

## Slide 12: System Requirements
Transmitter: minimal harmonic signals.
Propagation:
  Tissue harmonic imaging: maximal harmonic generation.
  Contrast imaging: minimal harmonic generation.
Receiver: maximal fundamental rejection.

## Slide 13: System Requirements
Adequate dynamic range.
Configurable beam former.
Sufficient system bandwidth.
Wide transducer bandwidth.

## Slide 14
Imaging Techniques
The phasing pattern across the array can be varied to reduce the signals at a certain frequency.
Alternate phasing is applicable to both tissue and contrast harmonic imaging.
Alternate phasing on transmit is not ideal.

## Slide 15: Imaging Techniques
Alternate phasing for receive:
0
0
0
0
0
0
0
0
0
0
0

0

0

0

0

Alternate phasing for transmit
0

0

0

0

0


## Slide 16: Imaging Techniques
Difference imaging technique: contrast agents can be viewed as a “modulator”. When two different frequencies, say f1 and f2, are used on transmit, the contrast agents generate f1+f2 and f1-f2.
f1 and f2 can be properly chosen to increase the rejection ratio.

## Slide 17: Imaging Techniques
In contrast imaging, in which the tissue harmonic signals are un-desirable, the amplitude of the propagating wave needs to minimized without sacrificing penetration.
Large apertures (smaller f-numbers) may be used.
It was reported that tissue harmonic signal can be reduced by 3dB by doubling the aperture size.

## Slide 18: Imaging Techniques
Harmonic cancellation system: non-linear propagation is reduced by using a new signal at the harmonic frequency.
Phase and magnitude of the signal may be pre-calculated, but on-line adjustment is necessary.
Due to attenuation, optimal effects may only be achieved locally.

## Slide 19: Imaging Techniques
Subtraction mode: Two pulses with different signs are transmitted consecutively. By adding two images together, linear components cancel while second order components remain.
This technique is susceptible to motion artifacts.

## Slide 20: Reduction of Imaging Artifacts
Due to the square nature of tissue harmonic generation, differences between mainlobe and sidelobes are inherently increased.
In the presence of aberrations, second harmonic imaging has proven to be effective in reducing the artifacts.
An alternative to current aberration correction techniques.

## Slide 21: Reduction of Imaging Artifacts

## Slide 22: Reduction of Imaging Artifacts