## Slide 1: Review of Ultrasonic Imaging

## Slide 2: Clinical Values of Ultrasound
Visualization of anatomical structures in real time.

## Slide 3: Clinical Values of Ultrasound
Detection of blood flows, including direction, velocity distribution, variance and energy.

## Slide 4: Clinical Values of Ultrasound
Estimation of mechanical properties such as strain, elasticity, attenuation, acoustic backscattering, …etc.
Treatment of diseased tissue by hyperthermia.
Treatment of stones by extracorporeal lithotripsy.

## Slide 5: Characteristics of Ultrasonic Imaging
Real-time.
Reflection mode.
Non-invasive.
Access limited.
Body type dependent.

## Slide 6: Factors of Image Quality
Spatial resolution.
Contrast resolution.
Temporal resolution.
Uniformity.
Sensitivity.
Penetration.

## Slide 7: Spatial Resolution
Lateral and elevational resolutions are diffraction limited as in optics.
Axial resolution is the width of the pulse. It is determined by system/transducer bandwidth and affected by attenuation.
Given limited total bandwidth, there exists a tradeoff between axial and lateral/elevational resolutions.

## Slide 8: Contrast Resolution
Contrast resolution is determined by both spatial resolution and speckle noise variations.
Speckle comes from coherent interference of diffuse scatterers. In-coherent processing must be used to reduce speckle noise.
There exists a tradeoff between contrast and spatial resolutions.

## Slide 9: Temporal Resolution
Temporal resolution is determined by acoustic frame rate. It is also related to spatial Nyquist criterion.
Temporal resolution is fundamentally limited by sound velocity but can be improved by signal processing in some cases.
There exists a tradeoff between temporal and spatial resolutions.

## Slide 10: Image Uniformity
Image uniformity is usually referred to as the variations of the system’s point spread function throughout the entire image.
Factors of image uniformity include depth of field, pulse shapes and variations due to lateral displacements.
To achieve image uniformity, a sophisticated imaging system is required.

## Slide 11: Sensitivity
Sensitivity is defined in the context of the detection of weak signals.
Sensitivity is determined by transducer design and system’s dynamic range.
Sensitivity is particularly important in Doppler imaging and can be improved by signal processing.

## Slide 12: Penetration
Penetration is determined by acoustic power delivered to the body on transmit and the dynamic range of the system on receive.
The transmit power is regulated for safety reasons. Hence, penetration must be improved without exceeding regulations.

## Slide 13: Course Contents: Diagnostic Ultrasound
Understanding the fundamental limitations.
Improving the image quality.
New technologies.
The future.

## Slide 14: Course Contents: Other Applications
Therapeutic ultrasound.
Transducer design and manufacturing.
Clinical applications - from M.D.’s point of view.